## Slide 1
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Monitoring
Oil & TSS in Water
&
BS & W in Oil
Through Dynamic Imaging Technology
JM Canty International

## Slide 2
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Oil & Sand in Produced Water - Background
Produced Water Analysis
Oil in Water
Environmental
TSS in Water
Process Control & Optimisation
Process Control & Optimisation
Separation Equipment / Chemical Performance Analysis
30ppm Dispersed Oil in Water
Separation Equipment Performance Analysis
WFI – TSS Size & Concentration Analysis to Avoid Well Plugging
Well Formation Studies – Core Sample Testing

## Slide 3
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- Water in Oil (PPM Concentration, Droplet Size)
Process Control & Optimisation
- Separator Performance Analysis
- Pipe Line Transfer Issues / Adherence to Refinery Standards
- Solids in Oil (PPM Concentration, Particle Size)
Pipe Line Transfer Issues / Adherence to Refinery Standards
Crude Oil Analysis - Background

## Slide 4: Vision Based Particle Analysis Basic Principle
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
JM Canty’s vision based technique works on the basic principle of presenting the fluid between a high intensity light source, and microscopic camera
The captured images are then sent to CantyVision Client Software for analysis, where the suspended particulate (oil or water, solids, gas bubbles etc.) is measured under a number of different parameters to provide size, shape and concentration data

## Slide 5
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Gigabit Ethernet technology for optimum image retrieval
1900 x 1200 Pixel Array configurable to 0.23µm per Pixel Resolution
Particle / Droplet Size to 0.7µm
Simple RJ45 Network Connection to Control PC
Image Retrieval – Hardware – CCD Camera
Sand in Water

## Slide 6
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Retrieval – Hardware– Lighting System
High flow rates inline require an increased shutter speed and so an increased amount of light to capture particulate in “freeze frame” in order to perform software analysis
High Intensity LED Light Source
5+ Years Continuous Operation
Flow velocity up to 5m/s

## Slide 7
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Fused one piece construction with no recesses or steps where product can adhere to and build up
Pressures to 600 BAR
Integral Jet Spray Ring
Adjustable Gap Size dependent on sample present
Image Retrieval – Hardware – Fused Glass Flow Path

## Slide 8
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 9
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
InFlow – Inline Permanent Installations
Inline InFlow mounts as permanent spool piece in main process pipeline
Can also be mounted on fast loop bypass line for larger process lines

## Slide 10
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
InFlow – At-Line Permanent Installation
InFlow mounts in compact flow loop – wafer or flange mount to pipeline
Single fluid take off & return point on pipeline

## Slide 11
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Inline / At-Line InFlow with Local Image Processing

## Slide 12
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Mobile InFlow Cart with Local Image Processing

## Slide 13
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
WP Portable InFlow – Temporary Test / Troubleshooting
½” Swagelok Connection (typical pipeline sample points)
Outlet flow to open drain or lower pressure return point (ensure flow through analyser)
Analysis software on local laptop

## Slide 14
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
ATEX ZONE 1 Transportable InFlow
Dimensions: Width: 520mm, Depth: 570mm, Height: 1580mm (Inflow in vertical position during transportation).
Width during operation: 1000mm (Inflow in horizontal position)

## Slide 15
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Lab Mini Cell Core Unit
Lab system for TSS particle size and count.

## Slide 16
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Analysis – Hardware – Vector Control Module
CantyVision Intelligent Analysis Software Pre-Installed and configured
Rackmount VCM can support two particle analysis systems
Multiple outputs
-4-20mA
-OPC (OPC UA now available)
-TCP/IP Modbus
-Video Display
Remote Support Functionality

## Slide 17
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
The retrieved images are analysed by the Vector Control Modle (VCM) running the CantyVision Intelligent Analysis Software
Each particle is analysed under a number of different parameters (major axis, minor axis, area, perimeter, circularity, aspect ratio….)
Software filters (size / shape) can be applied so only particles with the characteristics of oil, solids, or air bubbles are individually analysed
Developed new self teaching software algorithm for identifying oil droplets, solids and gas bubbles.
Image Analysis – CantyVision Intelligent Analysis Software (CVIA)

## Slide 18
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Differentiating between Solids, Liquids and Bubbles
Based on index of refraction; solid particles, water/oil droplets and gas bubbles can all be distinguished by Canty software based on the direct 2D images.
Delivering the TRUE particle size of the particles.
Solid Particle
Gas
Water/Light Oil Droplet
Shape Parameter | Value
Circularity | .70
Aspect Ratio | 2.23
% Holes Area | 0%
Shape Parameter | Value
Circularity | .33
Aspect Ratio | 1.0
% Holes Area | 25.5%
Shape Parameter | Value
Circularity | .13
Aspect Ratio | 1.0
% Holes Area | 92.5%
Shape Parameter | Value
Circularity | 1
Aspect Ratio | 1.0
% Holes Area | 0%
Heavy Oil Droplet

## Slide 19
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Canty Intelligent Analysis Software Interface
CantyVision Software is able to process images at high speed real time.
Software provides graphical trends in charts with statistical data for particles, droplets and gas.
Individual data charts and outputs.
- Particle size distribution,
- Particle shape
- Concentrations - counts per ml, ppm
Customized reporting feature for excel data output.

## Slide 20
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Analysis – CantyVision Intelligent Analysis Software
Particles are automatically classified using machine learning classification feature to identify and distinguish between solids, droplets and bubbles based 37 different measurements parameters (shape, particle intensity, surface roughness …..).
System self classifies removing operator error
Droplets
Solids
Gas Bubbles

## Slide 21
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Analysis – CantyVision Intelligent Analysis Software
Software can be set up with multiple classification parameters to detect the difference between different types of particles.
Easy to use graphical interface allows user to click on particles within the class they want to measure and sort particles by their individual classes.
Machine learning algorithms build a database of particle shape characteristics.

## Slide 22
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Analysis – CantyVision Intelligent Analysis Software
Real time particle size distribution and shape information charts
Real time volumetric concentration measurements charts
Particle count per ml charts
Multiple Charts depending on information required

## Slide 23
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
OIW/WIO Concentration
OIW < 0.5%
OIW 2%
OIW 40%

## Slide 24
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 1: Survey of Produced Water Plant
Test | Description
1 | Upstream & Downstream of Booster Pumps with Chemical Dosing
2 | Upstream & Downstream of Booster Pumps without Chemical Dosing
3 | Upstream & Downstream of Hydrocyclone with Chemical Dosing
4 | Upstream & Downstream of Hydrocyclone without Chemical Dosing
5 | Upstream & Downstream of LCV with Chemical Dosing
6 | Upstream & Downstream of LCV without Chemical Dosing
7 | Upstream & Downstream of CFU with Chemical Dosing
8 | Upstream & Downstream of CFU without Chemical Dosing
Objectives were to assess;
droplet shearing effect of Booster Pumps and Liquid Cylinder Valve
equipment performance for removal of oil droplets of varying size
effectiveness of coalescing chemical dosing

## Slide 25
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- Reduction in droplet size downstream vs upstream - pump shearing droplets
- Chemical dosing shown to have little influence on droplet size

## Slide 26
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- Reduction in droplet size downstream vs upstream as expected
- Chemical dosing shown to have little influence on droplet size

## Slide 27
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- No notable reduction in droplet size (no shearing) downstream vs upstream
- Chemical dosing shown to have little influence on droplet size

## Slide 28
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- No notable reduction in droplet size downstream vs upstream
- Chemical dosing shown to have little influence on droplet size

## Slide 29
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 2: Survey of an IGF & Nutshell Filter
The Canty Portable InFlow unit was connected to 3 different sampling points to determine if the inlet / outlet oil & solids were within specification;
IGF Inlet
IGF Outlet / Filter Inlet
Filter Outlet (Discharge Water)

## Slide 30
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
IGF Inlet IGF Outlet / Filter Inlet Filter Outlet
Case Study 2: Oil in Water
Dynamic Imaging Applied to IGF & Filtration Performance Analysis

## Slide 31
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 2: Survey of an IGF & Nutshell Filter

## Slide 32
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 3: Sand / TSS in WFI
Bu Hasa Field UAE, 200km SW of Abu Dhabi
Approximately 700 wells in total, with approximately 300 injection wells
Injection water is primarily taken from separate water supply well, some produced water injected also
Portable Inflow installed at sample points for approximately 2 hrs at a time
Real time results obtained compared with operator’s offline lab method

## Slide 33
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Sample Point 1: Cluster 30
TSS Size Data | 
Dv | Size (µm)
10 | 2.7
20 | 3.5
30 | 3.9
40 | 4.7
50 | 5.1
60 | 5.6
70 | 6.0
80 | 6.9
90 | 8.1
100 | 11.8
TSS Shape Data (Aspect Ratio) | 
Dv | 
10 | 1.19
20 | 1.27
30 | 1.33
40 | 1.40
50 | 1.51
60 | 1.61
70 | 1.69
80 | 1.76
90 | 1.88
100 | 2.84
Case Study 3: Sand / TSS in WFI

## Slide 34
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Sample Point 2: Cluster 49
TSS Size Data | 
Dv | Size (µm)
10 | 2.6
20 | 3.2
30 | 3.9
40 | 4.5
50 | 4.9
60 | 5.3
70 | 5.9
80 | 6.5
90 | 7.4
100 | 9.4
TSS Shape Data (Aspect Ratio) | 
Dv | 
10 | 1.27
20 | 1.30
30 | 1.36
40 | 1.44
50 | 1.52
60 | 1.59
70 | 1.68
80 | 1.74
90 | 1.84
100 | 2.69
Case Study 3: Sand / TSS in WFI

## Slide 35
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Sample Point 3: Cluster 51
TSS Size Data | 
Dv | Size (µm)
10 | 2.7
20 | 3.9
30 | 3.9
40 | 5.1
50 | 5.8
60 | 6.3
70 | 7.1
80 | 9.1
90 | 12.8
100 | 14.8
TSS Shape Data (Aspect Ratio) | 
Dv | 
10 | 1.24
20 | 1.28
30 | 1.33
40 | 1.39
50 | 1.45
60 | 1.60
70 | 1.59
80 | 1.73
90 | 1.88
100 | 3.33
Case Study 3: Sand / TSS in WFI

## Slide 36
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Recently , there have been intensive studies to determine water droplet size distribution along the 800 mile Alyeska Pipeline stretching from Purdue Bay to Valdez Alaska.
Over the years, crude flow has decreased significantly from the original design of 2 million barrels per day to the present 700,000 barrels per day.
This decrease in flow is a major cause of concern for water dropout. The volume of water, water droplet size and crude temperature are the major variables which determine the amount of water dropout in low-lying areas.
If water happens to accumulate in low-lying areas from reduction in flow or a pipeline shutdown, it could freeze and cause major restart issues and equipment damage.
Case Study 4: Measurement of Water Droplets in Crude

## Slide 37
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 38
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
As the crude reaches East Meters in Valdez, the line pressure ranges between 750 to 850 psi
The crude enters East Meters and passes through pressure reduction valves, dropping the pressure to approximately 120 psi
The Canty was installed to determine the effect of this pressure drop on water droplet size. This application also demonstrates the importance of choosing the correct process location to study droplet size
The Canty was installed at both the high pressure and low pressure side of the pressure reduction valves
Case Study 5: Effect of Pressure Reduction Valves on Water Droplets in Crude

## Slide 39
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Before Pressure Reduction Valves
Water Droplets Clearly Visible
Water Droplets Have Been Sheared
After Pressure Reduction Valves

## Slide 40: Questions & Answers
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621