## Slide 1: Canty Process Technology Glass Applications
Colleen Kelley, JM Canty Inc

## Slide 2: Overview
Brief Introduction to Canty
Molten Glass Level
Onion Skin Width
Exit End Width/Ribbon Width
ADS Edge Tracking
Hot End Melt Line
Questions

## Slide 3: Molten Glass Level
How it works?
CantyVision software has the capability to track the position of any edge.
For normal vessel applications it would track the edge between the vessel wall and the top of the process fluid.
Reflection issues with molten glass make it difficult to track the edge between the furnace wall and the surface of the molten glass.
Canty has developed a method whereby we measure the movement of a reflection of a stationary object such as a missing brick from the furnace wall.

## Slide 4: Molten Glass Level

## Slide 6: Onion Skin Width
Camera allows for the automated control of the position and shape at the initial draw in front of the tin bath (also known as the onion skin) resulting in a more uniform pull.
Result is less waste and higher efficiency for the glass.

## Slide 7: Onion Skin Video

## Slide 8: Glass Width

## Slide 9: Overview
Minimize trim loss – The Canty float glass system consists of a high temperature Ethernet process camera and incorporates special software to reduce glare along with a unique orifice plate that prevents debris from adhering to the lens, resulting in a clear view of the glass ribbon at all times.
This system is a non-contact web width control system which positions Ethernet cameras over the two glass edges and provides continuous real time measurement of web width as glass enters the Lehr annealing chamber after exiting the furnace chamber.
Width measurements are made in real-time on a continuous basis, with a resolution of .015". CantyVision™ Client Software utilizes image based technology to continually track the extreme edge of the glass ribbon and also the edge of the knurled region formed by the top roll machines used in the float bath furnace to shape and stabilize the glass ribbon.

## Slide 10: Technical Application

## Slide 11: Application Illustration & Layout

## Slide 12: Camera Installation & Orientation

## Slide 13: Camera Installation & Orientation Top Down View

## Slide 14: Camera Installation & Orientation Horizontal View

## Slide 15: Industrial Surveillance Camera Exploded Assembly

## Slide 16: VCM

## Slide 17: Vector Control Module Advantages
Allows for input up to 6 cameras
Allows for Cameras to run on Power Over Ethernet (POE) when directly connected via Cat 6 ethernet cable
Multiple outputs
-4-20mA
-OPC (OPC UA now available)
-Modbus
-Video Display
Camera heartbeat/Temperature Alarm
Ease of Remote Support

## Slide 18: ADS Edge Tracing
Control of Puller Utilizing existing periscope cameras, no additional cameras needed

## Slide 20: Hot End Melt Line

## Slide 21: Hardware
Canty ExtremeTemp™ Camera to view bath
Canty VCM for analysis

## Slide 23: Questions?