## Slide 1
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Monitoring
Oil & TSS in Water
Canty Process Technology

## Slide 2
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Oil & Solids in Water - Background
Water Analysis
Oil in Water
Environmental
TSS in Water
Process Control & Optimisation
Process Control & Optimisation
Separation Equipment / Chemical Performance Analysis
30ppm Dispersed Oil in Water
Separation Equipment Performance Analysis
WFI – TSS Size & Concentration Analysis to Avoid Well Plugging
Well Formation Studies – Core Sample Testing

## Slide 3: Vision Based Particle Analysis Basic Principle
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
JM Canty’s vision based technique works on the basic principle of presenting the fluid between a high intensity light source, and microscopic camera
The captured images are then sent to CantyVision Software for analysis, where the suspended “particles” (oil or water, solids, gas bubbles etc.) are measured for a number of different parameters to provide size, shape and concentration data

## Slide 4
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hardware – Image Retrieval and Analysis
Camera
Light
Flow Cell
Vector Control Module (VCM)
4 Primary Hardware Components Required For High Quality Image Analysis:

## Slide 5
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Gigabit Ethernet technology for optimum image retrieval
4112 x 2176 Pixel Array configurable to 0.23µm per Pixel Resolution
Particle / Droplet Size to 0.7µm
Simple RJ45 Network Connection to Control PC
Hardware – Image Retrieval
Camera
Sand in Water

## Slide 6
High flow rates inline require an increased shutter speed and so an increased amount of light to capture particulate in “freeze frame” in order to perform software analysis
High Intensity LED Light Source
5+ Years Continuous Operation
Flow velocity up to 5m/s
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hardware – Image Retrieval
Lighting System

## Slide 7
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Fused one piece construction with no recesses or steps where product can adhere to and build up
Pressures to 600 BAR
Integral Jet Spray Ring
Adjustable Gap Size dependent on sample present
Hardware – Image Retrieval
Fused Glass Flow Path

## Slide 8
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 9
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hardware – Image Analysis
Vector Control Module (VCM)
Ease of use and installation
Multiple analyzers from one VCM
Multiple outputs to interface with
Remote Support Functionality

## Slide 10
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations
Many different types of installations to adapt to where analysis is needed:
      Inline
      At-Line
      Skid
      Cart
      Portable
      Transportable
      Lab

## Slide 11
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – In-line
Directly in process
Acts as a spool piece in the pipe
Typically up to 2” lines
Can also be mounted on fast loop bypass line for larger process lines

## Slide 12
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – At-Line
Short Loop Sampler
  Wafer or flange models
Ability to isolate from process
One take out and return line
Line size 3”+

## Slide 13
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – Skid
Allows for full control of cleaning system
Can be an all-in-one installation for VCM, cleaning, power supply, and analyzer
Can be integrated with in-line and at-line systems

## Slide 14
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations - Cart
Long-term temporary testing
Mobile system
Includes cleaning pump
Functionally a skid system on wheels

## Slide 15
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – Portable
Short-term temporary testing
Easy to transport
General purpose
Analysis hardware built in PSU

## Slide 16
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations - Transportable
Short-term temporary testing
ATEX rated
Easy to move from sample point to sample point
VCM built into unit, accessed via ATEX tablet

## Slide 17
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations - Lab
Same technology applied for offline samples
Smaller flow cell for smaller sample volumes
Screen, VCM, and power supply all built into one unit
CSV file reports

## Slide 18
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Example OIW Concentration Images
OIW < 0.5%
OIW 2%
OIW 40%

## Slide 19
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Easy to use interface
Real time analysis
Video analysis options
Reports PSSD’s (particle size and shape distributions), concentrations
Software – Image Analysis
CantyVision Intelligent Analysis (CVIA)

## Slide 20
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
For each image in the analysis:
Distinguish background from “particles”
Throw out anything that is out of focus
Measure shape and size parameters of each particle
Determine the particle “class”
  Solid, oil droplet, gas bubble, etc…
Compile measurements (size, volume, etc…)
Update results
Software – Image Analysis
How does it work?

## Slide 21
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Based on particle morphology solid particles, oil droplets, and gas bubbles can all be distinguished by Canty software based on the direct 2D images.
Originally accomplished using a small number of shape parameters
Now accomplished via machine learning
Software – Image Analysis
Differentiating between Solids, Droplets, and Bubbles

## Slide 22
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Example particle images trained into software
40+ shape and size parameter trends analyzed
System self classifies removing operator error
Droplets
Solids
Gas Bubbles
Software – Image Analysis
Differentiating between Solids, Droplets, and Bubbles

## Slide 23
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Easy to build in multiple custom classes for specific R&D
Intuitive GUI allows user to click on particles within the class they want to measure and sort particles by their individual classes.
Software – Image Analysis
Differentiating between Solids, Droplets, and Bubbles

## Slide 24
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Analysis – Outputs
Real time PSSA, concentration display
  Percentiles
  Binned Distributions
  PPM
  PPML
Local CSV Report Outputs
Outputs can be sent via 4-20mA, Modbus TCP/IP, OPC UA, and others

## Slide 25
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
EPA Standard – Oil in Water
  EPA Method 1664, Revision B: n-Hexane Extractable Material (HEM; Oil and Grease) and Silica Gel Treated n-Hexane Extractable Material (SGT-HEM; Non-polar Material) by Extraction and Gravimetry
  Serves the industry well for offline samples
  Nothing currently available online – we see this as an important need
  Imaging seems to be the obvious choice to move forward

## Slide 26
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 1: Survey of Produced Water Plant
Test | Description
1 | Upstream & Downstream of Booster Pumps with Chemical Dosing
2 | Upstream & Downstream of Booster Pumps without Chemical Dosing
3 | Upstream & Downstream of Hydrocyclone with Chemical Dosing
4 | Upstream & Downstream of Hydrocyclone without Chemical Dosing
5 | Upstream & Downstream of LCV with Chemical Dosing
6 | Upstream & Downstream of LCV without Chemical Dosing
7 | Upstream & Downstream of CFU with Chemical Dosing
8 | Upstream & Downstream of CFU without Chemical Dosing
Objectives were to assess;
droplet shearing effect of Booster Pumps and Liquid Cylinder Valve
equipment performance for removal of oil droplets of varying size
effectiveness of coalescing chemical dosing

## Slide 27
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- Reduction in droplet size downstream vs upstream - pump shearing droplets
- Chemical dosing shown to have little influence on droplet size

## Slide 28
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- Reduction in droplet size downstream vs upstream as expected
- Chemical dosing shown to have little influence on droplet size

## Slide 29
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- No notable reduction in droplet size (no shearing) downstream vs upstream
- Chemical dosing shown to have little influence on droplet size

## Slide 30
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
- No notable reduction in droplet size downstream vs upstream
- Chemical dosing shown to have little influence on droplet size

## Slide 31
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 2: Survey of an IGF & Nutshell Filter
The Canty Portable InFlow unit was connected to 3 different sampling points to determine if the inlet / outlet oil & solids were within specification;
IGF Inlet
IGF Outlet / Filter Inlet
Filter Outlet (Discharge Water)

## Slide 32
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
IGF Inlet IGF Outlet / Filter Inlet Filter Outlet
Case Study 2: Oil in Water
Dynamic Imaging Applied to IGF & Filtration Performance Analysis

## Slide 33
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 2: Survey of an IGF & Nutshell Filter

## Slide 34
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Case Study 3: Sand / TSS in WFI
Bu Hasa Field UAE, 200km SW of Abu Dhabi
Approximately 700 wells in total, with approximately 300 injection wells
Injection water is primarily taken from separate water supply well, some produced water injected also
Portable Inflow installed at sample points for approximately 2 hrs at a time
Real time results obtained compared with operator’s offline lab method

## Slide 35
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Sample Point 1: Cluster 30
TSS Size Data | 
Dv | Size (µm)
10 | 2.7
20 | 3.5
30 | 3.9
40 | 4.7
50 | 5.1
60 | 5.6
70 | 6.0
80 | 6.9
90 | 8.1
100 | 11.8
TSS Shape Data (Aspect Ratio) | 
Dv | 
10 | 1.19
20 | 1.27
30 | 1.33
40 | 1.40
50 | 1.51
60 | 1.61
70 | 1.69
80 | 1.76
90 | 1.88
100 | 2.84
Case Study 3: Sand / TSS in WFI

## Slide 36
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Sample Point 2: Cluster 49
TSS Size Data | 
Dv | Size (µm)
10 | 2.6
20 | 3.2
30 | 3.9
40 | 4.5
50 | 4.9
60 | 5.3
70 | 5.9
80 | 6.5
90 | 7.4
100 | 9.4
TSS Shape Data (Aspect Ratio) | 
Dv | 
10 | 1.27
20 | 1.30
30 | 1.36
40 | 1.44
50 | 1.52
60 | 1.59
70 | 1.68
80 | 1.74
90 | 1.84
100 | 2.69
Case Study 3: Sand / TSS in WFI

## Slide 37
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Sample Point 3: Cluster 51
TSS Size Data | 
Dv | Size (µm)
10 | 2.7
20 | 3.9
30 | 3.9
40 | 5.1
50 | 5.8
60 | 6.3
70 | 7.1
80 | 9.1
90 | 12.8
100 | 14.8
TSS Shape Data (Aspect Ratio) | 
Dv | 
10 | 1.24
20 | 1.28
30 | 1.33
40 | 1.39
50 | 1.45
60 | 1.60
70 | 1.59
80 | 1.73
90 | 1.88
100 | 3.33
Case Study 3: Sand / TSS in WFI

## Slide 38: Questions & Answers
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621