## Slide 1
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Monitoring
Basic Sediment & Water (BS&W) in Oil
Canty Process Technology

## Slide 2: Vision Based Particle Analysis Basic Principle
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
JM Canty’s vision based technique works on the basic principle of presenting the fluid between a high intensity light source, and microscopic camera
The captured images are then sent to CantyVision Software for analysis, where the suspended “particles” (water droplets in oil, solids, gas bubbles etc.) are measured for a number of different parameters to provide size, shape and concentration data

## Slide 3
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hardware – Image Retrieval and Analysis
Camera
Light
Flow Cell
Vector Control Module (VCM)
4 Primary Hardware Components Required For High Quality Image Analysis:

## Slide 4
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Gigabit Ethernet technology for optimum image retrieval
4112 x 2176 Pixel Array configurable to 0.23µm per Pixel Resolution
Particle / Droplet Size to 0.7µm
Simple RJ45 Network Connection to Control PC
Hardware – Image Retrieval
Camera
Sand in Water

## Slide 5
High flow rates inline require an increased shutter speed and so an increased amount of light to capture particulate in “freeze frame” in order to perform software analysis
High Intensity LED Light Source
5+ Years Continuous Operation
Flow velocity up to 5m/s
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hardware – Image Retrieval
Lighting System

## Slide 6
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Fused one piece construction with no recesses or steps where product can adhere to and build up
Pressures to 600 BAR
Integral Jet Spray Ring
Adjustable Gap Size dependent on sample present
Hardware – Image Retrieval
Fused Glass Flow Path

## Slide 7
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 8
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hardware – Image Analysis
Vector Control Module (VCM)
Ease of use and installation
Multiple analyzers from one VCM
Multiple outputs to interface with
Remote Support Functionality

## Slide 9
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations
Many different types of installations to adapt to where analysis is needed:
      Inline
      At-Line
      Skid
      Cart
      Portable
      Transportable
      Lab

## Slide 10
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – In-line
Directly in process
Acts as a spool piece in the pipe
Typically up to 2” lines
Can also be mounted on fast loop bypass line for larger process lines

## Slide 11
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – At-Line
Short Loop Sampler
  Wafer or flange models
Ability to isolate from process
One take out and return line
Line size 3”+

## Slide 12
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – Skid
Allows for full control of cleaning system
Can be an all-in-one installation for VCM, cleaning, power supply, and analyzer
Can be integrated with in-line and at-line systems

## Slide 13
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations - Cart
Long-term temporary testing
Mobile system
Includes cleaning pump
Functionally a skid system on wheels

## Slide 14
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations – Portable
Short-term temporary testing
Easy to transport
General purpose
Analysis hardware built in PSU

## Slide 15
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations - Transportable
Short-term temporary testing
ATEX rated
Easy to move from sample point to sample point
VCM built into unit, accessed via ATEX tablet

## Slide 16
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Installations - Lab
Same technology applied for offline samples
Smaller flow cell for smaller sample volumes
Screen, VCM, and power supply all built into one unit
CSV file reports

## Slide 17
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Easy to use interface
Real time analysis
Video analysis options
Reports PSSD’s (particle size and shape distributions), concentrations
Software – Image Analysis
CantyVision Intelligent Analysis (CVIA)

## Slide 18
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
For each image in the analysis:
Distinguish background from “particles”
Throw out anything that is out of focus
Measure shape and size parameters of each particle
Determine the particle “class”
  Solid, water droplet, gas bubble, etc…
Compile measurements (size, volume, etc…)
Update results
Software – Image Analysis
How does it work?

## Slide 19
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Based on particle morphology solid particles, oil droplets, and gas bubbles can all be distinguished by Canty software based on the direct 2D images.
Originally accomplished using a small number of shape parameters
Now accomplished via machine learning
Software – Image Analysis
Differentiating between Solids, Droplets, and Bubbles

## Slide 20
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Example particle images trained into software
40+ shape and size parameter trends analyzed
System self classifies removing operator error
Droplets
Solids
Gas Bubbles
Software – Image Analysis
Differentiating between Solids, Droplets, and Bubbles

## Slide 21
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Easy to build in multiple custom classes for specific R&D
Intuitive GUI allows user to click on particles within the class they want to measure and sort particles by their individual classes.
Software – Image Analysis
Differentiating between Solids, Droplets, and Bubbles

## Slide 22
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Image Analysis – Outputs
Real time PSSA, concentration display
  Percentiles
  Binned Distributions
  PPM
  PPML
Local CSV Report Outputs
Outputs can be sent via 4-20mA, Modbus TCP/IP, OPC UA, and others

## Slide 23
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Comparison of methods to measure water in oil
  Crackle test
    Offline, qualitative, variability operator to operator
  Karl Fischer
    Offline (performed in hood), Requires reagents, Requires skilled lab tech, Time-consuming, No size distribution measured
  Calcium Hydride
    Offline, Requires reagents, No size distribution measured
  Relative Humidity
    Cannot measure free water, no particle size distribution
  Infrared
    Cannot measure free water and is heavily influenced by the presence of free water
  Dynamic Imaging
    Offline and Online, no reagents, measures free water concentration AND size distribution, measures TSS at the same time

## Slide 24
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Comparison of methods to measure water in oil
Technology | Offline/ Online | Requires Reagents | Measures Free Water | Measures TSS | Provides Size Distribution
Dynamic Imaging | Both | No | Yes | Yes | Yes
Karl Fischer | Offline Only (Lab) | Yes | Total water only | No | No
Infrared | Both | Sometimes | No* | No | No
Calcium Hydride | Offline Only | Yes | Total water only | No | No
Relative Humidity | Both | No | No | No | No
Crackle Test | Offline Only | No** | Qualitative only | No | No
*Infrared systems can be heavily impacted by the presence free water as the free droplets can scatter the spectrum.
**The crackle test does not require additional reagents, but it does require heating the sample.

## Slide 25
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Recently , there have been intensive studies to determine water droplet size distribution along the 800 mile Alyeska Pipeline stretching from Purdue Bay to Valdez Alaska.
Over the years, crude flow has decreased significantly from the original design of 2 million barrels per day to the present 700,000 barrels per day.
This decrease in flow is a major cause of concern for water dropout. The volume of water, water droplet size and crude temperature are the major variables which determine the amount of water dropout in low-lying areas.
If water happens to accumulate in low-lying areas from reduction in flow or a pipeline shutdown, it could freeze and cause major restart issues and equipment damage.
Case Study 1: Measurement of Water Droplets in Crude

## Slide 26
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 27
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
As the crude reaches East Meters in Valdez, the line pressure ranges between 750 to 850 psi
The crude enters East Meters and passes through pressure reduction valves, dropping the pressure to approximately 120 psi
The Canty was installed to determine the effect of this pressure drop on water droplet size. This application also demonstrates the importance of choosing the correct process location to study droplet size
The Canty was installed at both the high pressure and low pressure side of the pressure reduction valves
Case Study 2: Effect of Pressure Reduction Valves on Water Droplets in Crude

## Slide 28
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Before Pressure Reduction Valves
Water Droplets Clearly Visible
Water Droplets Have Been Sheared
After Pressure Reduction Valves

## Slide 29: Questions & Answers
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621