## Slide 1
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
HIGH TEMPERATURE CAMERAS
IN
FLOAT GLASS
Tod Canty Jr.
CANTY

## Slide 2: IMAGE PROCESSING APPLICATIONS
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Level
Width & Knurl
Gob & Temperature
Onion
Ribbon & Stone

## Slide 3: Key Features of Imaging Systems
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
High Temperature Reliability - Fused Glass
Maintenance – Spray Ring
Ethernet Connectivity
  Gigabit Camera
Lens Assembly
  Quartz or Sapphire Shield
High Resolution Imaging
  .001”
Integrated Software

## Slide 4: Key Features of Imaging Systems
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Hermetically sealed fused glass to protect the electronics

## Slide 5: Key Features of Imaging Systems
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
SprayRing to keep the fused glass lens clean.
  Instrument Clean Air is needed at 30PSI min required

## Slide 6: Key Features of Imaging Systems
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Lens assembly allows the Ethernet CCD camera to remain outside the process in ambient room temperature air vs being fixed in the higher temperature process air.

## Slide 7: Benefits of vision
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Less expensive than laser
More accurate –pixel scale factor
User friendly calibration
  Visual Verification
  Not trying to line up 2 devices

## Slide 8: Level
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
High Temperature Ethernet Camera
VCM with CANTY AI Software
Orfice Plate = No Maintenace
Replace platinum dipper probes, lasers, & nuclear systems
Resolution of 001".
Visual Verification
OPC or 4-20mA Output

## Slide 9: Level
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 10: Level
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 11: Level camera
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 12: Width & Knurl
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Determining the position of the total width is extremely important at the end of the furnace to determine total size. To effectively accomplish this the knurl must be measured and compared to the edge. The CANTY Ethernet cameras using CANTYVISION™ will monitor both width & knurl. This results in less waste and higher productivity for the glass when it comes to cutting the knurl. The camera system is able to effectively monitor and measure real time location of the width and knurl and provide a 4-20mA output or OPC to a PLC or DCS for complete automated control.

## Slide 13: Width & Knurl
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 14: Width & Knurl
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 15: Width & Knurl
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 16: Width & Knurl
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 17: Gob & Temperature
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
The CANTYVISION™ System is positioned on a glass bottle production line to monitor and control the glass gob volume and temperature. A glass gob is a still drop of molten glass formed by cutting a stream of glass as it flows from the fore hearth through a feeder of variable diameters. These gobs free fall into molds and create glass bottles. The volume and temperature of the gobs are critical to quality control and with the Canty Glass Gob analysis system all of these parameters can be controlled.

## Slide 18: Gob & Temperature
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 19: Gob & Temperature
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 20: Temperature
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 21: Temperature
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Through CantyVisionClient software the user can calibrate temperature measurements made with a handheld pyrometer through the software to produce real time temperature measurements.
A one-time calibration allows for continuous and accurate temperature feedback. Same as multi-wave pyrometers – except no emissivity problem.

## Slide 22: Onion
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
By controlling the position and shape at the initial draw in the front of the tin bath (also known as Onion Skin) results in more uniform pull. This results in less waste and higher efficiency for the glass. The camera system is able to effectively monitor and measure real time location of the onion and provide a 4-20mA output or OPC to a PLC or DCS for complete automated control.

## Slide 23: Onion
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 24: Onion
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 25: Ribbon & Stone
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
The purpose of the particle detection application is to determine when foreign debris has fallen onto the glass surface within the tin bath and alarm when debris is 0.125 inches in size or larger. Within the tin bath a sheet of glass floats on molten tin and occasionally a piece of refractory, insulation, etc., falls onto the glass. The debris will travel further downstream on top of the glass and the debris may hit a coater that is placed at the end of the tin bath. Typically the coater is set at height of 0.25 inches above the glass, so any debris larger than the gap between the coater and the glass can cause some major damage to the glass and the process.

## Slide 26: Ribbon & Stone
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 27: Ribbon & Stone
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621

## Slide 28: Conclusion
JM Canty, Inc. · Buffalo, New York · Phone: (716) 625-4227 | JM Canty, Ltd. · Dublin, Ireland · Phone: +353 (1) 882-9621
Real Time Measurement
Repeatable / Accurate
Visual Verification
Output Signals-ethernet,4-20ma,OPC
Process Control
Better Quality
Higher Yield